## Slide 1: Evolution of porosity, permeability and pore structure in mudstones upon fluid injection
Harsh Biren Vora
Dr. Brandon Dugan

## Slide 2: Fluid Injections in Mudstones
Motivation
Effective Stress
Lattice Boltzmann Modeling of Mudstone Permeability
Experimental results of fluid injection tests
Conclusions
Future Work

## Slide 3: Why study fluid injection ?
www.eia.gov
Notes: Wastewater injection

## Slide 4: Why study fluid injection ?
Problems associated with fluid injection:
  Induced seismicity,
  triggering of faults
  contamination of water reserves
Only 25-60 % of injected water is recovered at the surface (Gregory et. al, 2011; O’Malley et. al, 2016)
Renewed interest in shales as hydrocarbon reservoirs
Mudstones and shales make up 60% of sedimentary record (Pettijohn, 1957)
Oklahoma Geological Survey
Notes: Natural processes also cause unloading – heating, charging of reservoirs, hydrocarbon maturation, erosion and clay diagenesis

## Slide 5: Effective Stress Law
σeff : Effective stress
σV : Overburden stress
Pp: Pore pressure
σeff = σV - Pp
Goulty, 2002
Increasing σeff : Loading
Decreasing σeff: Unloading
Notes: Fluid injection is a process of unloading
Natural processes also cause unloading – heating, charging of reservoirs, hydrocarbon maturation, erosion and clay diagenesis

## Slide 6: Objectives
How do petrophysical signatures - k, φ, Vp and Vs – evolve upon unloading induced from fluid injection ?
Understand evolution of pore structure in mudstones upon fluid injection
Are there predictable pathways of accommodation of injected fluid in mudstones ?
Notes: What are the intermediate states of injection ?

## Slide 7: Methods – Lattice Boltzmann
Daigle and Dugan, 2011
Chuckwudzoe, 2011
k = permeability
<u> = flow velocity for unit length
ΔP = Pressure gradient
Notes: Top and bottom constant pressure boundaries
Bounce back scheme on sides

## Slide 8: LBM – Initial Model
φi = 0.07
kH = 406 nD
KV = 10.3 nD
w: grain width
t: grain thickness
ξ: inter-bed pore diameter (=t)
σ : pore throat diameter (=0.5*t)
2 μm
0.05 μm

## Slide 9: LBM – Isotropic Expansion
Injection affects all pores uniformly
Notes: Elastic behavior

## Slide 10: LBM – Micro-fracture growth
Opening of pore throats Expansion of interbed pores

## Slide 11: LBM – Fracture Propagation
Formation of high-conductivity pathway

## Slide 12: LBM Results
Chart: 
| -19.989514510736544 | -18.889078975422589 | -18.264800125426838 | -17.829428903119158 | -17.494360165702997 | -16.991629288091204 | -16.616982317387592 | -16.189244240203546 | -15.763493174533663
Dilation | 0.07 | 0.181 | 0.269 | 0.341 | 0.401 | 0.496 | 0.566 | 0.644 | 0.716
MF-parallel | 0.07 | 0.174 | 0.256 | 0.324 | 0.428 | 0.504 | 0.587 | 0.646
MF-perpendicular | 0.07 | 0.102 | 0.183 | 0.248 | 0.333 | 0.406 | 0.486 | 0.567 | 0.664
Frac-parallel | 0.07 | 0.174 | 0.256 | 0.353 | 0.428 | 0.504 | 0.587 | 0.662 | 0.708
Frac-perp | 0.07 | 0.123 | 0.213 | 0.318 | 0.407 | 0.471 | 0.545 | 0.616
Modified from Neuzil, 1994
φi = 7%
Notes: Comparable with contemporary results
Left of dilation/compaction line: storage parallel to bedding
Right of dilation/compaction line: storage perpendicular to bedding
Scale independence

## Slide 13: Takeaways from LBM Models
Model analogs for fluid injection yield permeability results comparable to contemporary data (Neuzil, 1994)
Φ vs k response changes significantly depending on dominating mechanism of accommodation of injected fluid
Developed LB model framework can be applied to experimental measurements of φ and k to predict pore structure evolution upon fluid injection
Notes: Resolvable by laboratory experiments

## Slide 14: Experimental Methods
Bhandari et. al., 2015
Petrophysical measurements:
Porosity (φ)
Permeability (k)
Acoustic velocity (Vp and Vs)

## Slide 15: Experimental Methods
Permeability (k)
Velocity (Vp and Vs)
Q = flowrate (m3/s)
k= permeability (m2)
Pu= Upstream Pressure (Pa)
Pd = Downstream Pressure (Pa)
µ = Viscosity (Pa.s)
L = length of sample (m)
Darcy, 1856
PU
PD
Vp more sensitive than Vs to fluid pressure
Vp and Vs are sensitive to pore structure changes
(Mavko et. al, 2009)
Bowers, 2005
Notes: Porosity is measured from injected fluid volume, fluid used is distilled water
P wave velocities tend to be more sensitive to pore fluid pressure, S to structural changes

## Slide 16: Experimental and Core Details
Core Details
IODP 308-1324B-3H4
Depth = 18.4 mbsf
Insitu Stress = 60.352 psi
φi = 65 %
Clay = 63.3 %
Silt = 36.6%
Sand = 0.1%
Notes: B tests

## Slide 17: Fluid Injection trends
Notes: Explain injection zones

## Slide 18: Porosity – Permeability trends
Notes: K is not a simple function of effective stress or proosity

## Slide 19: Unloading Stage 1
Chart: 
| -19.989514510736544 | -18.889078975422589 | -18.264800125426838 | -17.829428903119158 | -17.494360165702997 | -16.991629288091204 | -16.616982317387592 | -16.189244240203546 | -15.763493174533663
Dilation | 0.07 | 0.181 | 0.269 | 0.341 | 0.401 | 0.496 | 0.566 | 0.644 | 0.716
MF-parallel | 0.07 | 0.174 | 0.256 | 0.324 | 0.428 | 0.504 | 0.587 | 0.646
MF-perpendicular | 0.07 | 0.102 | 0.183 | 0.248 | 0.333 | 0.406 | 0.486 | 0.567 | 0.664
Frac-parallel | 0.07 | 0.174 | 0.256 | 0.353 | 0.428 | 0.504 | 0.587 | 0.662 | 0.708
Frac-perp | 0.07 | 0.123 | 0.213 | 0.318 | 0.407 | 0.471 | 0.545 | 0.616
Notes: Left of dilation – fluid stored parallel to bedding
Vp more sensitive than Vs – fluid pressure

## Slide 20
Unloading Stage 1
Notes: No significant change in structure

## Slide 21: Unloading Stage 2
Chart: 
| -19.989514510736544 | -18.889078975422589 | -18.264800125426838 | -17.829428903119158 | -17.494360165702997 | -16.991629288091204 | -16.616982317387592 | -16.189244240203546 | -15.763493174533663
Dilation | 0.07 | 0.181 | 0.269 | 0.341 | 0.401 | 0.496 | 0.566 | 0.644 | 0.716
MF-parallel | 0.07 | 0.174 | 0.256 | 0.324 | 0.428 | 0.504 | 0.587 | 0.646
MF-perpendicular | 0.07 | 0.102 | 0.183 | 0.248 | 0.333 | 0.406 | 0.486 | 0.567 | 0.664
Frac-parallel | 0.07 | 0.174 | 0.256 | 0.353 | 0.428 | 0.504 | 0.587 | 0.662 | 0.708
Frac-perp | 0.07 | 0.123 | 0.213 | 0.318 | 0.407 | 0.471 | 0.545 | 0.616
Notes: Velocity
Fracture porosity

## Slide 22
Unloading Stage 2
Notes: No significant change in structure

## Slide 23: Future Work: NMR
Katsube, 2000
NMR helps understand the pore-size distribution in rock
Notes: Methodology of NMR acquisition
Pore structure

## Slide 24: Future Work: NMR
Dilation
Micro-fracture growth
Fracture propagation
Correlation between developed model analogs and experimental results can be verified by imaging pore structure evolution
Initial NMR signature

## Slide 25: Future Work: Alternate Stress Paths
Current Analysis
Rate of Fluid Injection
Erosion
Effect of Stress Anisotropy

## Slide 26
Future Work: Elastic Properties
Mavko et. al, 2009

## Slide 27: Conclusions
Pore-scale LBM models replicate realistic porosity-permeability relationships in mudstones
For low overpressures, injected fluid is accommodated as isotropic expansion and parallel to bedding in a dilational/ micro-fracture mechanism – this may be elastic response
As pore pressures approach confining pressure, injected fluid is accommodated perpendicular to bedding by opening of pore throats leading to evolution of high conductivity pathways.
Notes: Hydraulic fracturing
k trends

## Slide 28: Future Work
k-φ relationships in compacted shales upon fluid injection.
NMR experiments to validate correlation between models and injection patterns, and image evolution of pore structure upon fluid injection
Alternate Stress paths to analyze effect of
  Rate of fluid injection
  Direction of injection w.r.t bedding
  Unloading from reducing confining pressure (erosion)
  Differential Pressure
Evolution of Elastic Properties to understand change in mechanical properties of rock